SonATA Integration and Test Plan
2010-05-10 jj

1. RFI scans with a single antenna 1200 Mhz to 9000 Mhz
Create Permanent RFI Mask

2. Determine signal detection thresholds for observing
Pulse - Get Pulse counts for quiet sky at pulse thresholds from 8 to 15.
Triplet -
CW Power
CW coherent (primary & secondary)

3. Verify signal gain provided by using the collecting area of multiple telescope
Observe Kepler (or equivalent spacecraft) with 4, 3, 2, and 1 antennas.

4. Verify beam sensitivity
Observe Kepler with 3 beams. Set offactnulls none and multitargetnulls off.
Compare the detections.

5. Collect statistics on Multibeam RFI rejection

6. Determine number of half frames for baseline initial accumulation
set baseintaccum from 5 to 20. Compare waterfalls.